## Slide 1: Bicycle Infrastructure Recommendations
Katelyn Schreyer
DATA 205
Spring 2021

## Slide 2: Cycleways

## Slide 3: Objectives
Identify roads or road segments with high numbers of bicyclist-involved incidents
Recommend which bicycle infrastructure improvements to prioritize that could prevent the greatest amount of collisions/injuries
  The Bicycle Master Plan already provides infrastructure recommendations considering what is feasible and appropriate to the road, but not which should be done first

## Slide 4: Datasets
Dataset | Provider | Description | Use for this project
Non-motorist collisions | dataMontgomery | Location, severity, and other details of accidents involving a bicyclist | Identify roads to examine, calculate incident rate
Roadway & Mapping Information | OpenStreetMap | Geospatial database of roads and map tiles | Collect roadway characteristics and tiles for mapping
Bicycle Master Plan | Montgomery Planning | Comprehensive survey of the streets in Montgomery County, including current Level of Traffic Stress (LTS) and bicycle infrastructure | Determine LTS of roadways where incidents occurred, existing bicycle infrastructure, planned bicycle infrastructure

## Slide 5: Methods
Compare incident severity to the Level of Traffic Stress (LTS) of the road segment at which they occurred
Calculate bicyclist-incidents-per-mile rate for every street in Montgomery County
Map incident locations and visually inspect the map for street segments or intersections with unusual incident clusters
Inspect high-incident roads or hotspots to see what infrastructure exists, if any, and what has been recommended.

## Slide 6: Key Results

## Slide 7: Key Results
Road Name | # Reported Incidents | Road Length (miles) | Incidents per mile
DORSET AVENUE | 7 | 1.25 | 5.59
STEDWICK ROAD | 5 | 1.50 | 3.33
FENTON STREET | 4 | 1.25 | 3.21
LITTLE FALLS PKWY | 8 | 2.50 | 3.20
ARDENNES AVENUE | 3 | 0.95 | 3.16
Incident per mile calculations:
Visually identified hotspots:
Road Name
Old Georgetown Road
Downtown Silver Spring
Little Falls Pkwy – Capital Crescent Trail
Georgia Ave between Ralph Rd and Heathfield Rd (Home Depot/Aspen Manor shopping area)
University Blvd – near Colesville Rd

## Slide 8: Little Falls Pkwy
Little Falls Pkwy
Capital Crescent Trail
7 of 8 incidents occurred at the Capital Crescent Trail crossing; 1 fatal
In 2017, bollards and additional signage was installed, and the number of lanes was reduced around the crossing
In 2020, a speed table crosswalk was completed; no incidents reported since
Recommendation: No further action

## Slide 9: Dorset Ave
1.25 miles
5.59 incidents per mile
  No serious injuries
Connects Wisconsin Ave and River Road
Provides access to Capital Crescent Trail
Potentially very high bike traffic?
Dorset Ave
Wisconsin Ave
River Rd
Recommendation: Add painted bike lane (low priority)
Capital Crescent Trail

## Slide 10: Old Georgetown Rd
Separated Bike Lane (highlighted) added from the Beltway to Cedar Rd in 2020 following a fatal collision in 2019
Cedar Road to Wisconsin Ave still has a high incident rate
Old Georgetown Rd
Wisconsin Ave
Cedar Rd
I-495
Recommendation: Extend separated bike lane to Wisconsin Ave (or to the Bethesda Trolley Trail)

## Slide 11: Georgia Ave (Ralph Rd to Heathfield Rd)
Collision Hotspots around the entrance to Home Depot and the Aspen Manor Shopping Center
Georgia Ave
Home Depot
Aspen Manor
Shopping Center
Connecticut Ave
Recommendation: Add separated bike lane

## Slide 12: Thank you!
dataMontgomery
  for making data available to the public and building a culture of data-aware and data-involved citizens
Montgomery Planning
  for the extensive work creating the Bicycle Master Plan
  for championing interventions that have saved lives
Montgomery College Professors
  Michael Iapalucci
  Rachel Saidi
  Abdirisak Mohamed